## Slide 1: Unmixing the Mixture with Next Generation Sequencing
International Symposium on Human Identification
Palm Beach, Florida
November, 2025
Kari R. Danser, MS
William P. Allan, MS
Mark W Perlin, PhD, MD, PhD
Cybergenetics © 2003-2025

## Slide 2
On April 7, 2014, gas station clerk Babul Kumer Saha was killed before the store was robbed.
Ohio v. Slater Howell
Notes: 5 person mixture

## Slide 3: DNA Evidence
DNA samples were collected from a gas pump button, a plastic bag, and a lottery cash register slot.

## Slide 4: Capillary Electrophoresis (CE)
Fragment analysis
PCR based
STR multiplex
Notes: Originally STRs were separated by gel
Now STRs are most commonly separated by capillary electrophoresis
cost effective, high throughput, and offers fast turn around
implemented worldwide
PCR
  Polymerase Chain Reaction (PCR) gave the ability to make hundreds of millions of copies of specific sequences of DNA in only a few hours
  An enzymatic process in which a specific region of DNA is replicated repeatedly to yield many copies of a particular sequence
  Involves heating and cooling in a precise thermal cycling pattern
  Under perfect conditions with 100% efficiency approximately a billion copies of the target sequence will be made
Multiplexing allows us to look at multiple STR locations in one reaction
Commercial kits were developing involving increasing numbers of STR locations

## Slide 5: TrueAllele on CE
Quantitative STR data at locus D10
peak
height
peak size

## Slide 6: Explaining the CE data
Seven-person DNA mixture

## Slide 7: CE Likelihood Ratio (22 loci)

## Slide 8: CE LR and error rate
A match between the plastic bag
and Slater Howell is:
98 thousand times more probable than a coincidental match.
For a match strength of 98 thousand,
only 1 in 119 million people would match as strongly.
Notes: Get the statement and error rate

## Slide 9: Case outcome
In 2017, the jury found Howell guilty. He was sentenced to life in prison.

## Slide 10: TrueAllele Reliability
Over 40 validation studies
  8 peer-reviewed publications
Validated for up 10 unknown contributors
49 successful US admissibility rulings
  16 different states
  3 Ohio Daubert hearings
  Federal court acceptance
  Appellate precedent in 8 states

## Slide 11: Next Generation Sequencing (NGS)
Sequence analysis
Bridge amplification
STR & SNP multiplex
Notes: Originally STRs were separated by gel
Now STRs are most commonly separated by capillary electrophoresis
cost effective, high throughput, and offers fast turn around
implemented worldwide
PCR
  Polymerase Chain Reaction (PCR) gave the ability to make hundreds of millions of copies of specific sequences of DNA in only a few hours
  An enzymatic process in which a specific region of DNA is replicated repeatedly to yield many copies of a particular sequence
  Involves heating and cooling in a precise thermal cycling pattern
  Under perfect conditions with 100% efficiency approximately a billion copies of the target sequence will be made
Multiplexing allows us to look at multiple STR locations in one reaction
Commercial kits were developing involving increasing numbers of STR locations

## Slide 13
Concordance (CE & NGS)
Single source
DNA mixture

## Slide 14: TrueAllele on NGS
Quantitative STR data at locus D12
peak height
peak size
Notes: New image with NGS data

## Slide 15: Explaining the NGS data
Seven-person DNA mixture
Notes: New image with NGS data and boxes

## Slide 16: NGS Likelihood Ratio (27 loci)
Notes: New image

## Slide 17: NGS LR and error rate
A match between the evidence item
and the defendant is:
29 million times more probable than a coincidental match.
For a match strength of 29 million,
only 1 in 12.4 billion people would match as strongly.

## Slide 18: CE vs. NGS
0
1
2
3
4
5
6
7
8
9
10
11
12
5.35
11.39
Victim
0
1
2
3
4
5
6
7
8
9
10
11
12
4.99
7.46
Suspect
More loci, more information
log(LR)

## Slide 19: Conclusions
TrueAllele inputs CE and NGS data
TrueAllele solves 10-person mixtures
NGS validation completed (2024)

## Slide 20
More information
http://www.cybgen.com/information
http://www.youtube.com/user/TrueAllele
TrueAllele YouTube channel
• Courses
• Newsletters
• Newsroom
• Presentations
• Publications
• Reliability
• Webinars